## Slide 1
MCU KNOWLEDGE
Inter-Processor Communication (IPC)
TRAVEO™ T2G B-H-8M MCU | KIT_T2G-B-H_LITE
BinhLV13 • May 2026

## Slide 2
1
Introduction to IPC
Enables multiple processors/cores to exchange data and coordinate tasks
Provides structured framework for reliable communication and sync
Improves scalability, maintainability, and deterministic operation
Implements locking to prevent race conditions and data corruption
Provides event-driven notifications via interrupts to reduce overhead
Channels handle commands, status, and data; interrupts signal events
Scope of this Document
This KB covers the IPC of the TRAVEO™ T2G B-H-8M MCU, included in the KIT_T2G-B-H_LITE kit.
Critical for automotive, industrial, telecom & embedded systems requiring multicore coordination and resource sharing.
IPC Knowledge Base | 2

## Slide 3
2
Abbreviations and Acronyms
Term | Description
CPUSS | CPU subsystem
IPC | Inter-processor communication
SMPU | Shared-Memory Protection Unit
SRAM | Static random-access memory
AHB | Advanced High-Performance Bus
FAQs | Frequently Asked Questions
IPC Knowledge Base | 3

## Slide 4
3
CPU Subsystem (CPUSS)
Heterogeneous subsystem: dual 32-bit Arm® Cortex®-M7 cores at 350 MHz
Plus one Cortex®-M0+ core at 100 MHz for peripheral/safety tasks
Each M7: 16 KB I-cache, 16 KB D-cache, 16 KB ITCM, 16 KB DTCM
Shared on-chip: ~8.4 MB code flash and 1 MB SRAM (SRAM0/1/2)
Multi-layer AXI/AHB interconnect arbitrates shared resource access
Hardware semaphores via IPC enable exclusive resource access
Key IPC-Related Hardware
Up to 8 hardware IPC channel registers (32 bytes each)
Matching IPC interrupt registers per channel
SMPU: up to 16 protected shared-SRAM regions
SRAM0 retainable in low-power modes
IPC Knowledge Base | 4

## Slide 5
4
IPC Mechanism
IPC hardware uses two register structures:
1
IPC Channel
Provides communication and synchronization between processors using six hardware registers.
2
IPC Interrupt
Each interrupt structure configures an interrupt line, triggerable by a 'notify' or 'release' event from any IPC channel.
IPC Knowledge Base | 5

## Slide 6
4.1
IPC Channel
Implemented as six hardware registers, accessible to all processors:
ACQUIRE
Acquires the lock; SUCCESS = 1 means lock acquired (atomic operation)
NOTIFY
Generates an IPC notify event; bits map to interrupt structures
RELEASE
Any write releases the channel; can trigger interrupt structures
DATA0 / DATA1
Two 32-bit registers for shared data or pointer to larger message
LOCK_STATUS
Instantaneous lock status: processor ID and protection context
IPC Knowledge Base | 6

## Slide 7
4.2
IPC Interrupt
Each IPC interrupt structure can be triggered by a notify or release event from any IPC channel. Sources can be masked via the interrupt registers.
INTR
Instantaneous status; 16 Notify + 16 Release event bits (max 16 channels). Write '1' clears it.
INTR_MASK
Masks interrupt sources; only enabled sources can trigger the interrupt
INTR_SET
Writing '1' sets the interrupt
INTR_MASKED
Logical AND of INTR and INTR_MASK; pending interrupts after masking
IPC Knowledge Base | 7

## Slide 8
4.3
IPC Channels and Interrupts
Each IPC interrupt register structure corresponds to an interrupt line
An interrupt line can interrupt any processor in the system
Interrupt routing for processors depends on device architecture
Each channel has release & notify registers driving interrupt events
A single channel's events can trigger multiple interrupt structures
IPC Knowledge Base | 8

## Slide 9
4.4
Implementing Locks
IPC channels implement mutual exclusion for shared resources
Processors acquire and release the channel to act as a lock
A processor must acquire the channel before accessing the resource
Failed acquisition = resource locked by another processor
Hardware does NOT enforce who acquires/releases the channel
Software must ensure the acquirer is also the releaser
IPC Knowledge Base | 9

## Slide 10
4.5
Message Passing
Sender (Processor A) → Receiver (Processor B), using channel lock + interrupts:
1
Sender reads ACQUIRE until SUCCESS = 1 — gains channel ownership
2
Sender writes message (up to 64 bits) into DATA0 / DATA1 registers
3
Sender sets bit in NOTIFY register — triggers interrupt on Receiver
4
Receiver reads INTR_MASKED, identifies channel, reads DATA0/DATA1
5
Receiver releases channel; may trigger release event on Sender
On the release interrupt, the sender may reacquire the channel or move to other tasks.
IPC Knowledge Base | 10

## Slide 11
4.5
Communicating Larger Messages
32-bit data registers limit direct message size
Larger messages: sender allocates structure in memory, passes pointer
User code must implement synchronization of the message read process
Option A: stall channel until receiver fully reads — wastes bandwidth
Option B: receiver releases channel right after getting the pointer
Sync via a flag — sender sets on write-complete, receiver clears on read-complete
IPC Knowledge Base | 11

## Slide 12
4.6
Registers
Register | Description
IPC_STRUCTx_ACQUIRE | Configures and acquires the lock
IPC_STRUCTx_RELEASE | Releases the lock
IPC_STRUCTx_NOTIFY | Generates notifications for interrupt structure
IPC_STRUCTx_DATA0 | 32-bit data element associated with IPC structure
IPC_STRUCTx_DATA1 | 32-bit data element associated with IPC structure
IPC_STRUCTx_LOCK_STATUS | Status of IPC (lock status, access mode, etc.)
IPC_INTR_STRUCTx_INTR | Status of the interrupts
IPC_INTR_STRUCTx_INTR_SET | Writing sets the corresponding INTR bit
IPC_INTR_STRUCTx_INTR_MASK | Mask bit for corresponding INTR bit
IPC_INTR_STRUCTx_INTR_MASKED | Bitwise AND of INTR and INTR_MASK
IPC Knowledge Base | 12

## Slide 13
5
Verification and Debugging
Reference: Verification-IPC.xlsx for verification/debugging details
Code example: message pipe using KIT_T2G-B-H_LITE kit (Fig. 8)
CM0+ is the primary CPU, responsible for system initialization
CM7_0 core calls cybsp_init() to initialize peripherals
CM7_0 force-releases lock via Cy_IPC_Drv_LockRelease, waits for CM0+ IPC server
CM7_0 sends notify interrupt → CM0+ performs LED ON/OFF, returns from ISR
IPC Knowledge Base | 13

## Slide 14
5.1
Frequently Asked Questions
Q
How many IPC channels/structures?
Up to 8 IPC channels and 8 interrupt structures, each with control, status, and data registers.
Q
How to configure an IPC channel/interrupt?
Configure CPUSS_CMx_SYSTEM_INT_CTL register, enable NVIC interrupt, implement handler.
Q
How is data synchronized between cores?
Hardware semaphores ensure exclusive access; SMPU + IPC signaling protect shared memory.
Q
Performance overhead?
Minimal latency/overhead; most time spent in the interrupt handler, not the IPC transfer.
Q
Errors or conflicts?
Hardware semaphores prevent simultaneous access; software handles retry/timeout/config errors.
Q
IPC during low-power or reset?
Available only when CPU subsystem is active; CM0+ initializes IPC before enabling CM7 cores.
IPC Knowledge Base | 14

## Slide 15
6
Reference & Revision History
Reference Documents
Document | Description
002-37237 Rev. *B, 2024-06-14 | KIT_T2G-B-H_LITE TRAVEO™ T2G Body High Lite Kit user guide
002-24401 Rev. *H, 2024-09-03 | TRAVEO™ T2G Automotive MCU body controller high architecture TRM
Revision History
Date | Revision | Changes
31-May-2026 | 1 | Initial release
IPC Knowledge Base | 15

## Slide 16
Summary
IPC provides channels (lock + data transfer) and interrupts (event signaling) for safe, efficient multicore coordination.
TRAVEO™ T2G B-H-8M: dual Cortex-M7 (350 MHz) + Cortex-M0+ (100 MHz), up to 8 IPC channels/interrupts
ACQUIRE/RELEASE registers implement atomic hardware locks for shared resources
DATA0/DATA1 carry 64-bit payloads directly, or pointers for larger messages
NOTIFY events trigger receiver interrupts; INTR_MASKED identifies the source channel
Software must enforce acquire/release symmetry — hardware does not restrict this
Reference TRM (002-24401) and kit guide (002-37237) for full register details